## Slide 1: Unmanned Aerial Vehicle Imaging System Creation For Water Quality Analysis
Victoria Scholl
Advisor: Aaron Gerace
Committee: David Long, Carl Salvaggio

## Slide 2: Outline
The Purpose
The Dream
The Team
The Progress
The Future

## Slide 3: The Purpose
Notes: Under the Clean Water Act, lists of impaired waters must be developed to identify waters that are too polluted to meet the water quality standards set by their states. The Rochester Embayment, primarily consisting of the region near where the Genesee River flows into the Lake Ontario Central Basin, is on the EPA’s impaired water list. Traditional remote sensing platforms have been used to monitor its water quality, but each has its serious limitations.

## Slide 4: The Purpose
NASA Jet Propulsion Lab Airborne Visible InfraRed Imaging Spectrometer
+ spectral resolution (224 bands, 400-2500nm)
- temporal resolution (once in 1999)
Notes: Rochester Embayment on EPA’s impaired waters list
Need for water quality and vegetation health analysis
Long-term, frequent monitoring desired
Existing satellites & airborne systems are not ideal (spatial / temporal resolution, collection pattern limitations)
Many other potential applications of system for CIS

## Slide 5: The Purpose
NASA Jet Propulsion Lab Airborne Visible InfraRed Imaging Spectrometer
+ spectral resolution (224 bands, 400-2500nm)
- temporal resolution (once in 1999)
NASA Landsat 8 satellite
+ temporal resolution (every 16 days)
- spectral/spatial resolution (30m pixels)
- limited by presence of atmosphere & clouds
Notes: Rochester Embayment on EPA’s impaired waters list
Need for water quality and vegetation health analysis
Long-term, frequent monitoring desired
Existing satellites & airborne systems are not ideal (spatial / temporal resolution, collection pattern limitations)
Many other potential applications of system for CIS

## Slide 6: The Purpose
NASA Jet Propulsion Lab Airborne Visible InfraRed Imaging Spectrometer
+ spectral resolution (224 bands, 400-2500nm)
- temporal resolution (once in 1999)
NASA Landsat 8 satellite
+ temporal resolution (every 16 days)
- spectral/spatial resolution (30m pixels)
- limited by presence of atmosphere & clouds
Multispectral UAV Imaging System
+ temporal resolution (whenever we want)
- spectral (any filters we want) /spatial resolution (1 inch pixels)
+ minimal atmosphere at low altitudes
Notes: Rochester Embayment on EPA’s impaired waters list
Need for water quality and vegetation health analysis
Long-term, frequent monitoring desired
Existing satellites & airborne systems are not ideal (spatial / temporal resolution, collection pattern limitations)
Many other potential applications of system for CIS

## Slide 7: The Dream
Fully functioning system and capture workflow
Develop calibration protocol
Image transfer, conversion, stitching
Near real-time, in-water constituent mapping

## Slide 8: The Team
Students
    Liz Bondi (Land) & myself (Water)

## Slide 9: The Team
Students
    Liz Bondi (Land) & myself (Water)
Research Experience
    Aaron Gerace, CIS
    Carl Salvaggio, CIS
    Matt Montanero, NASA

## Slide 10: The Team
Students
    Liz Bondi (Land) & myself (Water)
Research Experience
    Aaron Gerace, CIS
    Carl Salvaggio, CIS
    Matt Montanero, NASA
Drone ownership & operation
    Zeke Hurd and Mickey
    PJ (Papa Jeff Ring)
Notes: Zeke is hoping to start a business with the system, and Papa Jeff.
Liz is responsible for vegetation health efforts (primarily metrics such as NDVI), while I am working with the water imagery (constituent mapping).

## Slide 11: The Team

## Slide 12: The Progress
Over the summer:
Wrote funding proposal. CIS MicroGrant awarded ($5000)
Band selection analysis started over the summer
Camera acquired, complications with initial testing

## Slide 13: The Progress
Tetracam Micro Multi-Camera Array Snap ($20,000)
  6 compact, synchronized digital cameras
  16GB memory card per camera
  1.3 megapixel CMOS sensors (1280x1024), 10-bit DC
  Each bandpass filter ($1,300)
  1 master (set exposure time and geo-referencing), 5 slaves (set relative to master)
  PixelWrench2 software for image transfer and processing requires Windows 8
  Focal Length: 9.6mm
  Global shutter

## Slide 14: The Progress
Documenting how to use the Tetracam:
  Gain, exposure time, format, capture mode

## Slide 15: The Progress
Calibration
To use the imagery for scientific purposes, we have to equate digital count to a quantity of interest: reflectance

## Slide 16: The Progress
Calibration
To use the imagery for scientific purposes, we have to equate digital count to a quantity of interest: reflectance
ELM (Empirical Line Method)
Interpolate between dark and light targets of known reflectance
Pixel DC
Reflectance %

## Slide 17: The Progress
Calibration
To use the imagery for scientific purposes, we have to equate digital count to a quantity of interest: reflectance
ELM (Empirical Line Method)
Interpolate between dark and light targets of known reflectance
Pixel DC
Reflectance %

## Slide 18: The Progress
0%
16%
60%
Shaded
Sunlit

## Slide 19: The Progress
Calibration Target Paint Reflectance
  Light, Land: 60%
  Light, Water: 16%
  Dark: 0%
Notes: One of my tasks during the early weeks of this semester was to create the targets of known reflectance for calibration.
This involved calculating how large they need to be (which was determined to be 2x2’ for a flight altitude of 200ft), buying wood and getting it cut to the appropriate size, and finding the right paint. The paint should be spectrally flat, meaning it reflects equally at all wavelengths (at least the visible and NIR, which is what the Tetracam is sensitive to). Krylon makes an “ultra flat” black spray paint that is perfect but finding a lighter gray proved to be challenging.
We want different “light” grays for each application (water vs. veg) based on the maximum reflectance of each subject of interest. We tested out a variety of different paints and measured their spectral reflectance with an SVC spectometer.

## Slide 20: The Progress
Calibration Target Paint Reflectance
  Light, Land: 60%
  Light, Water: 16%
  Dark: 0%
Notes: One of my tasks during the early weeks of this semester was to create the targets of known reflectance for calibration.
This involved calculating how large they need to be (which was determined to be 2x2’ for a flight altitude of 200ft), buying wood and getting it cut to the appropriate size, and finding the right paint. The paint should be spectrally flat, meaning it reflects equally at all wavelengths (at least the visible and NIR, which is what the Tetracam is sensitive to). Krylon makes an “ultra flat” black spray paint that is perfect but finding a lighter gray proved to be challenging.
We want different “light” grays for each application (water vs. veg) based on the maximum reflectance of each subject of interest. We tested out a variety of different paints and measured their spectral reflectance with an SVC spectometer.

## Slide 21: The Progress
Calibration Target Paint Reflectance
  Light, Land: 60%
  Light, Water: 16%
  Dark: 0%
Notes: One of my tasks during the early weeks of this semester was to create the targets of known reflectance for calibration.
This involved calculating how large they need to be (which was determined to be 2x2’ for a flight altitude of 200ft), buying wood and getting it cut to the appropriate size, and finding the right paint. The paint should be spectrally flat, meaning it reflects equally at all wavelengths (at least the visible and NIR, which is what the Tetracam is sensitive to). Krylon makes an “ultra flat” black spray paint that is perfect but finding a lighter gray proved to be challenging.
We want different “light” grays for each application (water vs. veg) based on the maximum reflectance of each subject of interest. We tested out a variety of different paints and measured their spectral reflectance with an SVC spectometer.

## Slide 22: The Progress
Calibration Target Paint Reflectance
  Light, Land: 60%
  Light, Water: 16%
  Dark: 0%
Notes: One of my tasks during the early weeks of this semester was to create the targets of known reflectance for calibration.
This involved calculating how large they need to be (which was determined to be 2x2’ for a flight altitude of 200ft), buying wood and getting it cut to the appropriate size, and finding the right paint. The paint should be spectrally flat, meaning it reflects equally at all wavelengths (at least the visible and NIR, which is what the Tetracam is sensitive to). Krylon makes an “ultra flat” black spray paint that is perfect but finding a lighter gray proved to be challenging.
We want different “light” grays for each application (water vs. veg) based on the maximum reflectance of each subject of interest. We tested out a variety of different paints and measured their spectral reflectance with an SVC spectometer.

## Slide 23: The Progress
Calibration Target Paint Reflectance
  Light, Land: 60%
  Light, Water: 16%
  Dark: 0%
Notes: One of my tasks during the early weeks of this semester was to create the targets of known reflectance for calibration.
This involved calculating how large they need to be (which was determined to be 2x2’ for a flight altitude of 200ft), buying wood and getting it cut to the appropriate size, and finding the right paint. The paint should be spectrally flat, meaning it reflects equally at all wavelengths (at least the visible and NIR, which is what the Tetracam is sensitive to). Krylon makes an “ultra flat” black spray paint that is perfect but finding a lighter gray proved to be challenging.
We want different “light” grays for each application (water vs. veg) based on the maximum reflectance of each subject of interest. We tested out a variety of different paints and measured their spectral reflectance with an SVC spectometer.

## Slide 24: The Progress
Hardware prep
Tetracam tripod mount

## Slide 25: The Progress
Hardware prep
6 wooden calibration targets, painted, with tripod mounts
Exposure target

## Slide 26: The Progress
Protocol for setting exposure
  Need to manually set exposure time (microseconds)
  Auto-exposure means imagery is not scientifically meaningful

## Slide 27: The Progress

## Slide 28: The Progress
Test Sites

## Slide 29: The Progress

## Slide 30: The Progress
Spreading Wings S900 drone
Max flight time: 22 minutes

## Slide 31: The Progress
Test Flight and Initial Aerial Capture

## Slide 32: The Progress
Setting up Calibration Targets

## Slide 33: The Progress
Setting Exposure

## Slide 34: The Progress
Flight over Maier’s Farm Soybean Field

## Slide 35: The Progress
Imaging Long Pond

## Slide 36: The Progress
Imaging Long Pond

## Slide 37: The Progress
Same-day Landsat collection, water samples taken

## Slide 38: The Progress
Challenges in the field
  Windows Updates
  Efficient exposure method determined for vegetation
  Inefficient exposure method determined for water
  Manual flight renders imagery useless
  No GPS information

## Slide 39: The Progress

## Slide 40: The Future
Setting exposure for water scenes
  Complications arise since the 800nm IR band is the master
  Tetracam was designed for imaging vegetation
  MODTRAN modeling in progress

## Slide 41: The Future
Setting exposure for water scenes
  Complications arise since the 800nm IR band is the master
  Tetracam was designed for imaging vegetation
  MODTRAN modeling in progress
Calibration
  Make flags
  Develop automated calibration routine
      Feature recognition (targets)
      Extract pixel values
      Apply ELM
      Test runs

## Slide 42: The Future
Setting exposure for water scenes
  Complications arise since the 800nm IR band is the master
  Tetracam was designed for imaging vegetation
  MODTRAN modeling in progress
Calibration
  Make flags
  Develop automated calibration routine
      Feature recognition (targets)
      Extract pixel values
      Apply ELM
      Test runs
Water quality analysis
  Mosaic over water
  Multispectral analysis

## Slide 43: The Future
● Writing grant proposal for funding
● Modeling to determine spectral bands most pertinent to water quality analysis
● Acquisition and integration of hardware components
● Learning to operate UAS & program flight collection paths
● Ground truth data collection
● ELM Calibration to account for atmospheric effects
● Collaboration with other academic institutions for measurements
● Stitching together collected imagery
● Programming algorithms to extract water quality information from imagery
● Producing RGB and in-water constituent map for scene
Anticipated to be involved in the following:
KEY
Completed
In progress
Not yet attempted
Likely not going to be involved

## Slide 44: Questions / Comments?